Specification HPOE-460

Model HPOE-460 Hardware Interface “Data” Input Ports: 4 x RJ-45 “Data+Power” Output Ports: 4 x RJ-45 Data Rate 10/100/1000Mbps LED System: Power x 1 (Green) Per PoE Port: PoE ready / in-use x 4 (Green) Network Cable 10Base-T: 4-Pair UTP Cat. 5 up to 100m (328ft) 100Base-TX: 4-Pair UTP Cat. 5 up to 100m (328ft) 1000Base-T: 4-Pair UTP Cat. 5e, 6, up to 100m (328ft) EIA/TIA- 568 100-ohm STP (100m, 328ft) Dimension (W x D x H) 26 x 70 x 97 mm Weight 220g Power Requirement DC 52V~56V Power over Ethernet PoE Power Supply Type Mid-Span PoE Power Output Per Port DC 52V 30.8 Watts / 15.4 Watts Power Pin Assignment 4/5(+), 7/8(-) PoE Power Budget 120 Watts Number of 802.3af PD Class 0, 1, 2, 3 can be powered 4 Number of 802.3at PD Class 1, 2, 3 can be powered 4 Number of 802.3at PD Class 0, 4 can be powered 4 Standards Conformance Standards Compliance IEEE 802.3 10Base-T Ethernet IEEE 802.3u 100Base-TX Fast Ethernet IEEE 802.3ab 1000Base-T Gigabit Ethernet IEEE 802.3at Power over Ethernet (Pre-standard) IEEE 802.3af Power over Ethernet Regulation Compliance FCC Part 15 Class B, CE Environment Operating Temperature 0 ~ 50 Degree C Storage Temperature -10 ~ 70 Degree C Humidity 5 ~ 95% (Non-condensing)