Specification ICA-HM316W

Model ICA-HM316W Camera Specification Image Device 1/3.2" 2Mega-Pixel CMOS Sensor Effective Pixels 1600 x 1200 pixels Sensitivity 0.5lux Lens 3.6 ~ 16mm Vari-Focal lens with auto iris and IR cut filter/ F1.2 Illuminator 0 Lux IR on View Angle H: 20.8~75.4 Degree V: 15.7~54.9 Degree Video Specification Video Encoder H.264, MPEG4 and Motion JPEG simultaneously (Tri-encoders) Video Profile 12 profiles simultaneously - H.264 UXGA / 720p / SXGA/ VGA / QVGA / QCIF - M-JPEG UXGA / 720p / SXGA/ VGA / QVGA - MPEG4 QCIF (Only for 3GPP) Frame Rate UXGA Up to 15fps SXGA Up to 22fps HD-720p / SVGA / VGA / QVGA / QCIF Up to 30fps Image Setting Brightness, sharpness, contrast, AGC, BLC, Night Mode Text, time and date overlay Streaming Simultaneously multi-profile streaming M-JPEG streaming over HTTP Supports 3GPP mobile surveillance Controllable frame rate and bandwidth Constant and variable bit rate (MPEG4 / H.264) Audio Specification Audio Encoder RTSP:G.711 3GPP:AMR Audio Streaming One-Way or Two-Way Microphone External microphone input Audio Output Phone Jack Network Specification Network Standard IEEE 802.3, IEEE 802.3u IEEE 802.11b/g/n Supported Protocols TCP, UDP, HTTP, SMTP, FTP, NTP, DNS, DDNS, DHCP, UPnP, RTSP, RTP, RTCP, PPPoE, 3GPP, ICMP Security Password protection, user access log Users 10 simultaneous unicast users Ethernet 10/100M auto negotiation Antenna connector 2d Dipole Antenna Frequency 2.4GHz RF Transmit Power OFDM: 14 dBm CCK: 17 dBm Receiver Sensitivity 11b→1M: -90 11M: -85 11g→6M: -87 54M: -70 11n (BW20)→MCS0: -85 MCS7: -67 11n (BW40)→MCS0: -84 MCS7: -64 Data Rate IEEE 802.11b Standard Data Rates: 1, 2, 5.5 and 11Mbps IEEE 802.11g Standard Data Rates: 6, 9, 12, 18, 24, 36, 48, 54Mbps IEEE 802.11n Standard Data Rates: Legacy and High Throughput Modes, supports 20 / 40MHz Bandwidth MCS0~7 (150Mbps PHY Rate Rate) Security WEP 64/128, WPA, WPA2, TKIP, AES System Integration Application Programming Interface Open API for software integration SDK Alarm Triggers Intelligent video motion detection and external input Motion Detection 3-zone video motion detection Alarm Events File upload via FTP, email and save to MicroSD Card External output activation Video Buffer Pre- 5 sec and post- 10 sec alarm buffering General Power Supply 12V DC external power adapter Connectors RJ-45 10BaseT/100BaseTX DC jack 1 x RP-SMA Illumination LED IR LEDS IR LED Infrared LED ×35pcs IR Wavelength 850nm IR Distance 25M Power Consumption IR on: 6.24W IR off: 4.44W Protection Class IP-66 classification Operating Temperature -20 ~ 50 Degree C Viewing System OS Windows® XP, Vista 32bit, Win7 32bit, Server 2003 Browser IE 6.0 or latter Cell Phone With 3GPP player Video Player VLC, Quick Time, Real Player Software Specification Monitor/ Recording / Management PLANET CV3P (2-ch Cam Viewer 3 Pro Trail Version) PLANET CV3L (64-ch Cam Viewer 3 Lite Bundle Version) Search & Installation PLANET IP Installer

Specification

Model ICA-HM316W Camera Specification Image Device 1/3.2" 2Mega-Pixel CMOS Sensor Effective Pixels 1600 x 1200 pixels Sensitivity 0.5lux Lens 3.6 ~ 16mm Vari-Focal lens with auto iris and IR cut filter/ F1.2 Illuminator 0 Lux IR on View Angle H: 20.8~75.4 Degree V: 15.7~54.9 Degree Video Specification Video Encoder H.264, MPEG4 and Motion JPEG simultaneously (Tri-encoders) Video Profile 12 profiles simultaneously - H.264 UXGA / 720p / SXGA/ VGA / QVGA / QCIF - M-JPEG UXGA / 720p / SXGA/ VGA / QVGA - MPEG4 QCIF (Only for 3GPP) Frame Rate UXGA Up to 15fps SXGA Up to 22fps HD-720p / SVGA / VGA / QVGA / QCIF Up to 30fps Image Setting Brightness, sharpness, contrast, AGC, BLC, Night Mode Text, time and date overlay Streaming Simultaneously multi-profile streaming M-JPEG streaming over HTTP Supports 3GPP mobile surveillance Controllable frame rate and bandwidth Constant and variable bit rate (MPEG4 / H.264) Audio Specification Audio Encoder RTSP:G.711 3GPP:AMR Audio Streaming One-Way or Two-Way Microphone External microphone input Audio Output Phone Jack Network Specification Network Standard IEEE 802.3, IEEE 802.3u IEEE 802.11b/g/n Supported Protocols TCP, UDP, HTTP, SMTP, FTP, NTP, DNS, DDNS, DHCP, UPnP, RTSP, RTP, RTCP, PPPoE, 3GPP, ICMP Security Password protection, user access log Users 10 simultaneous unicast users Ethernet 10/100M auto negotiation Antenna connector 2d Dipole Antenna Frequency 2.4GHz RF Transmit Power OFDM: 14 dBm CCK: 17 dBm Receiver Sensitivity 11b→1M: -90 11M: -85 11g→6M: -87 54M: -70 11n (BW20)→MCS0: -85 MCS7: -67 11n (BW40)→MCS0: -84 MCS7: -64 Data Rate IEEE 802.11b Standard Data Rates: 1, 2, 5.5 and 11Mbps IEEE 802.11g Standard Data Rates: 6, 9, 12, 18, 24, 36, 48, 54Mbps IEEE 802.11n Standard Data Rates: Legacy and High Throughput Modes, supports 20 / 40MHz Bandwidth MCS0~7 (150Mbps PHY Rate Rate) Security WEP 64/128, WPA, WPA2, TKIP, AES System Integration Application Programming Interface Open API for software integration SDK Alarm Triggers Intelligent video motion detection and external input Motion Detection 3-zone video motion detection Alarm Events File upload via FTP, email and save to MicroSD Card External output activation Video Buffer Pre- 5 sec and post- 10 sec alarm buffering General Power Supply 12V DC external power adapter Connectors RJ-45 10BaseT/100BaseTX DC jack 1 x RP-SMA Illumination LED IR LEDS IR LED Infrared LED ×35pcs IR Wavelength 850nm IR Distance 25M Power Consumption IR on: 6.24W IR off: 4.44W Protection Class IP-66 classification Operating Temperature -20 ~ 50 Degree C Viewing System OS Windows® XP, Vista 32bit, Win7 32bit, Server 2003 Browser IE 6.0 or latter Cell Phone With 3GPP player Video Player VLC, Quick Time, Real Player Software Specification Monitor/ Recording / Management PLANET CV3P (2-ch Cam Viewer 3 Pro Trail Version) PLANET CV3L (64-ch Cam Viewer 3 Lite Bundle Version) Search & Installation PLANET IP Installer