Specification FNSW-1600P

Model FNSW-1600P Hardware Specification Network Connector 16-Port RJ-45 for 10/100Base-TX PoE Inject Port 16 LED Display System: Power (Green) Per port : PoE (Orange) LNK/ACT (Green) Switch Architecture Store and Forward switch architecture MAC Address 8K MAC address table with Auto learning function Switch Fabric 3.2Gbps Switch Throughput 2.38Mpps@64Bytes Power Requirement AC 100~240V, 50/60Hz, 2A max. Power Consumption Max.135 Watts / 460 BTU Dimension (W x D x H) 445 x 207 x 45 mm (1U height) Weight 2.33kg Power over Ethernet PoE Standard IEEE 802.3af Power over Ethernet PoE Power Supply Type Mid-Span, PSE PoE Power Output Per Port 48V DC, 350mA. Max. 15.4 Watts Power Pin Assignment 4/5(-), 7/8(+) PoE Power Budget 125 Watts Standard Conformance EMI Safety FCC Class A, CE Standard Compliance IEEE 802.3: Ethernet IEEE 802.3u: Fast Ethernet IEEE 802.3x: Flow Control IEEE 802.3af: Power over Ethernet Environment Operating environment 0 ~ 50 Degree C Storage environment -40 ~ 70 Degree C Operating Humidity 5 ~ 95%, relative humidity, non-condensing Storage Humidity 5 ~ 95%, relative humidity, non-condensing