Specification

Model ICA-HM101 Camera Image Sensor 1/3" 2 Mega-Pixel CMOS image sensor Lens 4.3 mm, F1.8 View Angle H: 56 Degree V: 43 Degree Effective Pixels 1600 x 1200 (UXGA) Min Illumination 0.5 lux @ F1.2 Signal to Noise 42 dB LED 12 x White-light LED Indication LED Green ：LAN LED Orange ：Power / Wireless LED PIR Sensor Built-in 6m / 120 Degree Coverage Motion Detection 10 area definable Video Video Encoder H.264 / MPEG-4 / M-JPEG Video Profile 20 profiles simultaneously Video Resolution H.264 UXGA / VGA / QVGA / QQVGA MPEG4 VGA / QVGA / QQVGA M-JPEG UXGA / VGA / QVGA / QQVGA Rate Control CBR (Constant Bit Rate) / VBR (Variable Bit Rate) Frame Rate Mega-Pixel mode up to 15fps for all resolution VGA mode up to 30fps for VGA / QVGA / QQVGA Image Setting AE, AWB 3D Noise Reduction Digital WDR Color, Brightness, Sharpness, Contrast, Hue Mirror / Flip Privacy Masks Text, Time and Date Overlay Streaming Simultaneous multi-profile streaming Streaming over UDP, TCP, or HTTP M-JPEG streaming over HTTP (server push) Supports 3GPP mobile surveillance (MPEG4) Controllable frame rate and bandwidth Constant and variable bit rate (MPEG4 / H.264) ROI Audio Audio Codec RTSP: G.711 64kbps, G.726 32kbps 3GPP: AMR Audio Streaming One-Way or 2-Way Audio I/O Audio in: Internal Microphone and Speaker Audio out: Line Network and Configuration Network Interface 10/100M auto negotiation Network Standard IEEE 802.3 IEEE 802.3u Network Protocol TCP/IP, UDP, HTTP, SMTP, FTP, NTP, DNS, DDNS, DHCP, DIPS ARP, Bonjour, UPnP, RTSP, RTP, RTCP, IGMP, PPPoE, 3GPP, ICMP, Samba Browser / Software Microsoft ® Internet Explorer 6.0 or later, PLANET Cam Viewer 3 Lite / Pro (CV3L . CV3P) Users 20 simultaneous unicast users Connection type Static IP, DHCP Management Web, CV3P, CV3L System Integration SDK Open API for software integration ONVIF Alarm Triggers Intelligent Video Motion Detection External Input PIR detector (Human Detect) Alarm Events File upload via FTP, Samba, SD card or email Notification via email, HTTP, and TCP External output activation Audio alerting output Video Buffer Pre and post alarm buffering Environment Power Requirement 12V DC, 1A IEEE 802.3af Dimension (W x D x H) 91 x 58 x 39 x 91mm Weight 146g Power Consumption 6W (12VDC) Operating Temperature -10 ~ 40 Degree C Operating Humidity 20 ~ 80% (non-condensing) Emission CE, FCC

Specification