IGS-10080MFT

| SFP/mini-GBIC Slots | 8 100/1000Base-SX/LX mini-GBIC SFP slots |
| --- | --- |
| Copper Ports | 2 10/100/1000Base-T Ethernet interface |
| Switch Architecture | Store-and-Forward |
| Switch Fabric | 20Gbps / non-blocking |
| Throughput (packet per second) | 14.8Mpps |
| Address Table | 8K entries, automatic source address learning and ageing |
| Flow Control | IEEE 802.3x Pause Frame for Full-Duplex. Back pressure for Half-Duplex |
| Jumbo Frame | 9Kbytes |
| Reset Button | < 5 sec: System reboot > 5 sec: Factory Default |
| ESD Protection | 6KV DC |
| EFT Protection | 6KV DC |
| Enclosure | IP30 Aluminum Metal Case |
| Installation | DIN Rail Kit and Wall Mount Kit |
| Alarm | One relay output for power fail Alarm Relay current carry ability: 1A @ DC 24V |
| LED Indicators | System: Power 1 (Green) Power 2 (Green) Fault Alarm (Green) Ring (Green) * R.O. (Green) * Per 10/100/1000T RJ-45 Ports: 1000 (Green) 10/100, LNK/ACT (Orange) Per SFP Interface: 1000 LNK/ACT(Green) 100 LNK/ACT (Orange) |
| Dimension (W x D x H) | 152 x 107x 72mm |
| Weight | 1036g |
| Power Requirement | DC 12 to 48V, AC 24V Power Adapter |
| Power Consumption | 13.92 Watts / 47.76BTU (Full loading) |
| Layer 2 function |
| Basic Management Interfaces | Web Browser, Remote Telnet, SNMP v1, v2c |
| Secure Management Interface | SSH, SSL, SNMP v3 |
| Port configuration | Port disable/enable Auto-Negotiation 10/100/1000Mbps full and half duplex mode selection Auto-Detection / Forced 100/1000Mbps SFP Fiber transceiver speed Flow Control disable / enable Power saving mode control |
| Port Status | Display each port’s speed duplex mode, link status, Flow control status, Auto negotiation status, trunk status |
| Port Mirroring | TX / RX / Both Many to 1 monitor |
| E.R.P.S. Ring * | Recovery time <20ms |
| VLAN | 802.1Q Tagged Based VLAN, up to 255 VLAN groups Q-in-Q tunneling Private VLAN MAC-Based VLAN Protocol-Based VLAN Voice VLAN MVR (Multicast VLAN Registration) Up to 255 VLAN groups, out of 4095 VLAN IDs |
| Link Aggregation | IEEE 802.3ad LACP / Static Trunk Supports 5 groups of 10-Port trunk |
| QoS | Traffic classification based, Strict priority and WRR 8-Level priority for switching - Port Number - 802.1p priority - 802.1Q VLAN tag - DSCP field in IP Packet |
| IGMP Snooping | IGMP (v1/v2/V3) Snooping, up to 255 multicast Groups IGMP Querier mode support |
| MLD Snooping | MLD (v1/v2) Snooping, up to 255 multicast Groups MLD Querier mode support |
| Access Control List | IP-Based ACL / MAC-Based ACL Up to 256 entries |
| Bandwidth Control | Per port bandwidth control Ingress: 500Kb~1000Mbps Egress: 500Kb~1000Mbps |
| SNMP MIBs | RFC-1213 MIB-II RFC-2236 IGMPv2 RFC-2710 MLDv1 RFC-3376 IGMPv3 RFC-2879 RMON 1, 2, 3, 9 RFC-1493 Bridge MIB RFC-1643 Ethernet MIB RFC-2863 Interface MIB RFC-2665 Ether-Like MIB RFC-2819 RMON MIB (Group 1, 2, 3 and 9) RFC-2737 Entity MIB RFC-2618 RADIUS Client MIB RFC3411 SNMP-Frameworks-MIB IEEE 802.1X PAE IF-MIB LLDP MAU-MIB |
| Standards Conformance |
| Regulation Compliance | FCC Part 15 Class A, CE |
| Stability Testing | IEC60068-2-32 (Free fall) IEC60068-2-27 (Shock) IEC60068-2-6 (Vibration) |
| Standards Compliance | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX / 100Base-FX IEEE 802.3z Gigabit SX/LX IEEE 802.3ab Gigabit 1000T IEEE 802.3x Flow Control and Back pressure IEEE 802.3ad Port trunk with LACP IEEE 802.1D Spanning Tree Protocol IEEE 802.1w Rapid Spanning Tree Protocol IEEE 802.1s Multiple Spanning Tree Protocol IEEE 802.1p Class of service IEEE 802.1Q VLAN Tagging IEEE 802.1x Port Authentication Network Control IEEE 802.1ab LLDP |
| Environment |
| Operating | Temperature: -40 ~ 75 Degree C Relative Humidity: 5 ~ 95 % (Non-condensing) |
| Storage | Temperature: -40 ~ 75 Degree C Relative Humidity: 5 ~ 95 % (Non-condensing) |