Specification Model IGSW-2840 Hardware Specification 10/100Mbps Copper Ports 24 x 10/100Base-TX RJ-45 Auto-MDI / MDI-X ports 1000Mbps Copper Ports 4 x 10/100/1000Mbps RJ-45 Auto-MDI / MDI-X ports SFP / mini-GBIC Slots 4 x 1000Base-SX/LX/BX, shared with Port-25~28, Port -25, Port-26 compatibled with 100Base-FX SFP Switch Architecture Store-and-Forward Switch Fabric 12.8Gbps / Non-Blocking Switch Throughput 9.52Mpps @64Bytes Address Table 8K entries Share Data Buffer 2 Mbits Flow Control Back Pressure for Half-Duplex IEEE 802.3x Pause Frame for Full-Duplex LED Power, Link / Act and Speed Per Port Reset Button < 5 sec: System Reboot > 10 sec: Factory Default Dimension ( W x D x H) 440 x 200 x 44 mm, 1U height Weight 2.8 KG Power Requirement Redundant Power System: 12~48V DC and 110~240V AC Layer 2 Function Management Interface Console, Telnet, SSH, Web Browser, SSL, SNMPv1, v2c and v3 Port Configuration Port disable / enable Auto-Negotiation 10/100/1000Mbps Full and Half duplex mode selection Flow Control disable / enable Port Status Display each port’s speed duplex mode, link status and Flow control status Auto negotiation status, trunk status Bandwidth Control Input Rate Limit Output Traffic Shaper Allow to configure per 10K or 1M VLAN IEEE 802.1Q Tag-based VLAN IEEE 802.1v Protocol based VLAN Q-in-Q tunneling GARP / GVRP for VLAN Management Up to 255 VLANs groups, out of 4041 VLAN IDs Private VLAN Edge (PVE) supported Link Aggregation Supports 12 groups of 8-Port trunk, IEEE 802.3ad LACP QoS Traffic classification based on TCP / UDP Port Number, 802.1p priority, DSCP / TOS field in IP Packet IGMP Snooping IGMP (v1/v2) Snooping, up to 256 multicast Groups Access Control List IP-Based ACL / MAC-Based ACL In / Out direction per port Up to 32 rules per ACL SNMP MIBs RFC-1213 MIB-2 RFC-2863 Interface MIB RFC-2665 EtherLike MIB RFC-1493 Bridge MIB RFC-2674 Extended Bridge MIB RFC-2819 RMON MIB (Group 1, 2, 3,9) RFC-2737 Entity MIB RFC-2618 RADIUS Client MIB Standards Conformance Regulation Compliance FCC Part 15 Class A, CE Standard Compliance IEEE 802.3：10Base-T IEEE 802.3u：100Base-TX IEEE 802.3z：1000Base- SX/LX IEEE 802.3ab：1000Base-T IEEE 802.3x：Flow Control and Back pressure IEEE 802.3ad：Port trunk with LACP IEEE 802.1D：Spanning Tree protocol IEEE 802.1w：Rapid Spanning Tree protocol IEEE 802.1s：Multiple Spanning Tree protocol IEEE 802.1p：Class of service IEEE 802.1Q：VLAN Tagging IEEE 802.1v：Protocol VLAN IEEE 802.1x：Port Authentication Network Control IEEE 802.1ab：LLDP Environment Operating Temperature: -30 ~ 75 Degree C (DC) 0 ~ 70 Degree C (AC) Relative Humidity: 20 ~ 95% (non-condensing) Storage Temperature: -40 ~ 85 Degree C Relative Humidity: 20 ~ 95% (non-condensing) Model FGSW-2620VMP4 Hardware Specification 10/100Mbps Copper Ports 24 10/100Base-TX RJ-45 Auto-MDI / MDI-X ports 1000Mbps Copper Ports 2 10/100/1000Mbps RJ-45 Auto-MDI / MDI-X ports SFP / mini-GBIC Slots 2 1000Base-SX/LX/BX, shared with Port-25~Port-26 Switch Architecture Store-and-Forward Switch Fabric 8.8Gbps / non-blocking Switch Throughput 6.547Mpps @64Bytes Address Table 8K entries Share Data Buffer 512Kbytes Maximum Frame Size 9K Bytes Flow Control Back pressure for Half-Duplex IEEE 802.3x Pause Frame for Full-Duplex LED Power, FAN Alarm Link / Activity (Green) PoE In-Use (Amber) 1000 LNK / ACT(Green) 10/100 LNK / ACT(Green) Dimension (W x D x H) 440 x 300 x 44 mm, 1U height Weight 4.2kg Reset Button < 5 secs: System reboot > 10 secs: Factory Default Power Input 100 ~ 240VAC, 50 / 60Hz, Auto-sensing Power Consumption 400 Watts / 1372.4 BTU Power over Ethernet PoE Standard IEEE 802.3af Power over Ethernet / PSE PoE Power Supply Type End-Span Power Pin Assignment 1/2(+), 3/6(-) PoE Power Output Per Port 48V DC, 350mA . Max. 15.4 Watts PoE Power Budget 380 Watts Max. number of Class 2 PD 24 Max. number of Class 3 PD 24 Layer 2 Function Management Interface Console, Telnet, Web Browser, SSL, SNMPv1, v2c Port Configuration Port disable / enable Auto negotiation 10/100/1000Mbps full and half duplex mode selection Flow Control disable / enable Port Status Display each port’s speed duplex mode, link status and Flow control status Auto negotiation status, trunk status Port Mirroring TX / RX / Both 1 to 1 monitor Bandwidth Control Ingress / Egress Rate Control Allow to configure per 128Kbps VLAN IEEE 802.1Q Tag-based VLAN Port-based VLAN Q-in-Q tunneling Up to 255 VLANs groups, out of 4041 VLAN IDs Link Aggregation Supports 13 groups of 8-Port trunk, IEEE 802.3ad LACP QoS Traffic classification based on Port priority, 802.1p priority, DSCP / TOS field in IP Packet IGMP Snooping IGMP (v1/v2) Snooping, up to 256 multicast Groups Access Control List IP-Based ACL / MAC-Based ACL Up to 220 ACL rule entries SNMP MIBs RFC-1213 MIB-II RFC-2863 Interface MIB RFC-2665 EtherLike MIB RFC-1493 Bridge MIB RFC-2819 RMON MIB (Group 1, 2, 3,9) RFC-2737 Entity MIB POWER-ETHERNET-MIB Standards Conformance Regulation Compliance FCC Part 15 Class A, CE Safety UL, cUL Standards Compliance IEEE 802.3：10Base-T IEEE 802.3u：100Base-TX IEEE 802.3z：1000Base- SX/LX IEEE 802.3ab：1000Base-T IEEE 802.3x：Flow Control and Back Pressure IEEE 802.3ad：Port trunk with LACP IEEE 802.1D：Spanning Tree Protocol IEEE 802.1w：Rapid Spanning Tree Protocol IEEE 802.1p：Class of Service IEEE 802.1Q：VLAN Tagging IEEE 802.1x：Port Authentication Network Control RFC 768：UDP RFC 793：TFTP RFC 791：IP RFC 792：ICMP RFC 2068：HTTP RFC 1112：IGMP version 1 RFC 2236：IGMP version 2 Environment Operating Temperature: 0 ~ 50 Degree C Relative Humidity: 20 ~ 95% (non-condensing) Storage Temperature: -10 ~ 85 Degree C Relative Humidity: 20 ~ 95% (non-condensing)

Model FGSW-2620VMP4 Hardware Specification 10/100Mbps Copper Ports 24 10/100Base-TX RJ-45 Auto-MDI / MDI-X ports 1000Mbps Copper Ports 2 10/100/1000Mbps RJ-45 Auto-MDI / MDI-X ports SFP / mini-GBIC Slots 2 1000Base-SX/LX/BX, shared with Port-25~Port-26 Switch Architecture Store-and-Forward Switch Fabric 8.8Gbps / non-blocking Switch Throughput 6.547Mpps @64Bytes Address Table 8K entries Share Data Buffer 512Kbytes Maximum Frame Size 9K Bytes Flow Control Back pressure for Half-Duplex IEEE 802.3x Pause Frame for Full-Duplex LED Power, FAN Alarm Link / Activity (Green) PoE In-Use (Amber) 1000 LNK / ACT(Green) 10/100 LNK / ACT(Green) Dimension (W x D x H) 440 x 300 x 44 mm, 1U height Weight 4.2kg Reset Button < 5 secs: System reboot > 10 secs: Factory Default Power Input 100 ~ 240VAC, 50 / 60Hz, Auto-sensing Power Consumption 400 Watts / 1372.4 BTU Power over Ethernet PoE Standard IEEE 802.3af Power over Ethernet / PSE PoE Power Supply Type End-Span Power Pin Assignment 1/2(+), 3/6(-) PoE Power Output Per Port 48V DC, 350mA . Max. 15.4 Watts PoE Power Budget 380 Watts Max. number of Class 2 PD 24 Max. number of Class 3 PD 24 Layer 2 Function Management Interface Console, Telnet, Web Browser, SSL, SNMPv1, v2c Port Configuration Port disable / enable Auto negotiation 10/100/1000Mbps full and half duplex mode selection Flow Control disable / enable Port Status Display each port’s speed duplex mode, link status and Flow control status Auto negotiation status, trunk status Port Mirroring TX / RX / Both 1 to 1 monitor Bandwidth Control Ingress / Egress Rate Control Allow to configure per 128Kbps VLAN IEEE 802.1Q Tag-based VLAN Port-based VLAN Q-in-Q tunneling Up to 255 VLANs groups, out of 4041 VLAN IDs Link Aggregation Supports 13 groups of 8-Port trunk, IEEE 802.3ad LACP QoS Traffic classification based on Port priority, 802.1p priority, DSCP / TOS field in IP Packet IGMP Snooping IGMP (v1/v2) Snooping, up to 256 multicast Groups Access Control List IP-Based ACL / MAC-Based ACL Up to 220 ACL rule entries SNMP MIBs RFC-1213 MIB-II RFC-2863 Interface MIB RFC-2665 EtherLike MIB RFC-1493 Bridge MIB RFC-2819 RMON MIB (Group 1, 2, 3,9) RFC-2737 Entity MIB POWER-ETHERNET-MIB Standards Conformance Regulation Compliance FCC Part 15 Class A, CE Safety UL, cUL Standards Compliance IEEE 802.3：10Base-T IEEE 802.3u：100Base-TX IEEE 802.3z：1000Base- SX/LX IEEE 802.3ab：1000Base-T IEEE 802.3x：Flow Control and Back Pressure IEEE 802.3ad：Port trunk with LACP IEEE 802.1D：Spanning Tree Protocol IEEE 802.1w：Rapid Spanning Tree Protocol IEEE 802.1p：Class of Service IEEE 802.1Q：VLAN Tagging IEEE 802.1x：Port Authentication Network Control RFC 768：UDP RFC 793：TFTP RFC 791：IP RFC 792：ICMP RFC 2068：HTTP RFC 1112：IGMP version 1 RFC 2236：IGMP version 2 Environment Operating Temperature: 0 ~ 50 Degree C Relative Humidity: 20 ~ 95% (non-condensing) Storage Temperature: -10 ~ 85 Degree C Relative Humidity: 20 ~ 95% (non-condensing)