Specification IPOE-162S

Model IPOE-162S Hardware Specification Interface “PoE (Power + Data)” Input Port : 1 x RJ-45 10/100/1000Base-T “Data” Out Port: 1 x RJ-45 10/100/1000Base-T DC Out Plug Connector: 1 removable 4-Pin terminal block LED Indicator System: Power Ready x 1 (Green) Network Cable 10/100/1000Base-T: 4-Pair UTP Cat. 5, 5e, 6 Distance up to 100m (328ft) EIA/TIA- 568 100-ohm STP (100m) Data Rate 10/100/1000Mbps (vary on Ethernet device attached) DIP Switch 12V DC / 24V DC output voltage Power Input 802.3at PoE 48~56V DC Power Output 12V / 24V DC, Max 2A (adjustable) Dimension (W x D x H) 135 x 87.8 x 32 mm Weight 421g Enclosure IP30 Metal Case Installation DIN Rail Kit and Wall Mount Ear ESD / EFT Protection 6KV DC Power over Ethernet PoE Standard IEEE 802.3at High Power over Ethernet Number of device can be powered 1 or 2 (Vary on Device’s Power Requirement, DC1 + DC2 can not over 25Watts ) Standards Conformance Standards Compliance IEEE 802.3 10Base-T Ethernet IEEE 802.3u 100Base-TX Fast Ethernet IEEE 802.3ab 1000Base-T Gigabit Ethernet IEEE 802.3at High Power over Ethernet Regulation Compliance FCC Part 15 Class A, CE Stability Testing IEC60068-2-32(Free fall) IEC60068-2-27(Shock) IEC60068-2-6(Vibration) Environment Operating Temperature -40 ~ 75 Degree C Storage Temperature -40 ~ 85 Degree C Humidity 5 ~ 95% (Non-condensing)