| Hardware Specification WGSW-20160HP |
| --- |
| Copper Ports | 16 10/ 100/1000Base-T RJ-45 Auto-MDI/MDI-X ports |
| 10/100/1000Mbps / SFP Combo Interfaces | 4 10/100/1000Mbps TP and SFP shared combo interfaces, SFP(Mini-GBIC) supports 100/1000Mbps Dual mode, shared with Port-17 to Port-20 |
| Console | 1 x RS-232 DB9 serial port (115200, 8, N, 1) |
| Switch Architecture | Store-and-Forward |
| Switch Fabric | 40Gbps / non-blocking |
| Throughput | 29.7Mpps@64Bytes |
| Address Table | 8K entries, automatic source address learning and ageing |
| Share Data Buffer | 4 megabits |
| Flow Control | IEEE 802.3x Pause Frame for Full-Duplex Back pressure for Half-Duplex |
| Jumbo Frame | 9Kbytes |
| Reset Button | < 5 sec: System reboot > 5 sec: Factory Default |
| Dimension (W x D x H) | 440 x 300 x 44.5 mm, 1U high |
| Weight | 4.1kg |
| LED | System: Power (Green), SYS (System, Green) Alert: FAN1 (Green), FAN2 (Green) PoE Ethernet Interfaces (Port 1 to Port 16): LNK/ACT (10/100/1000Mbps, Green), PoE In-Use (Orange) 10/100/1000Base-T Combo Ports (Port 17 to port 20): 1000 (LNK/ACT, Green), 10/100 (LNK/ACT, Orange) 100/1000Mbps SFP Combo Interfaces (Port 17 to Port 20): 1000 (LNK/ACT, Green), 100 (LNK/ACT, Orange) |
| Power Requirement | 100~240V AC, 50/60Hz, 2A |
| Power Consumption | Max 22 Watts / 75BTU |
| ESD Protection | 6KV DC |
| Power over Ethernet |
| PoE Standard | IEEE 802.3af / 802.3at PoE / PSE |
| PoE Power Supply Type | End-Span |
| PoE Power Output | Per Port 56V DC Max. 30.8 Watts |
| Power Pin Assignment | 1/2(+), 3/6(-) |
| PoE Power Budget | 230 Watts Max. |
| PoE Ability | Number of PD @ 7 Watts: 16 Number of PD @ 15.4 Watts: 14 Number of PD @ 30.8 Watts: 7 |
| Layer 2 Management Function |
| Basic Management Interfaces | Console, Telnet, Web Browser, SNMP v1, v2c |
| Secure Management Interfaces | SSH, SSL, SNMP v3 |
| Port Configuration | Port disable / enable Auto-Negotiation 10/100/1000Mbps full and half duplex mode selection Flow Control disable / enable |
| Port Status | Display each port’s speed duplex mode, link status, Flow control status, Auto negotiation status, trunk status |
| Port Mirroring | TX / RX / Both Many-to-1 monitor |
| VLAN | 802.1Q Tagged Based VLAN, up to 255 VLAN groups Q-in-Q tunneling Private VLAN Edge (PVE) MAC-Based VLAN Protocol-Based VLAN Voice VLAN MVR (Multicast VLAN Registration) Up to 255 VLAN groups, out of 4094 VLAN IDs |
| Link Aggregation | IEEE 802.3ad LACP / Static Trunk Supports 10 groups of 16-Port trunk support |
| QoS | Traffic classification based, Strict priority and WRR 8-Level priority for switching Port Number 802.1p priority 802.1Q VLAN tag DSCP/TOS field in IP Packet |
| IGMP Snooping | IGMP (v1/v2/v3) Snooping, up to 255 multicast Groups IGMP Querier mode support |
| MLD Snooping | MLD (v1/v2) Snooping, up to 255 multicast Groups MLD Querier mode support |
| Access Control List | IP-Based ACL / MAC-Based ACL Up to 256 entries |
| Bandwidth Control | Per port bandwidth control Ingress: 500Kb~80Mbps Egress: 64Kb~80Mbps |
| SNMP MIBs | RFC-1213 MIB-II IF-MIB RFC-1493 Bridge MIB RFC-1643 Ethernet MIB RFC-2863 Interface MIB RFC-2665 Ether-Like MIB RFC-2819 RMON MIB (Group 1, 2, 3 and 9) RFC-2737 Entity MIB RFC-2618 RADIUS Client MIB RFC-2933 IGMP-STD-MIB RFC-3411 SNMP-Frameworks-MIB IEEE 802.1X PAE LLDP MAU-MIB |
| Standards Conformance |
| Regulation Compliance | FCC Part 15 Class A, CE |
| Standards Compliance | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX/100Base-FX IEEE 802.3z 1000Base-SX/LX IEEE 802.3ab 1000Base-T IEEE 802.3x Flow Control and Back pressure IEEE 802.3ad Port trunk with LACP IEEE 802.1D Spanning tree protocol IEEE 802.1w Rapid spanning tree protocol IEEE 802.1s Multiple spanning tree protocol IEEE 802.1p Class of service IEEE 802.1Q VLAN Tagging IEEE 802.1x Port Authentication Network Control IEEE 802.1ab LLDP IEEE 802.3af Power over Ethernet IEEE 802.3at Power over Ethernet PLUS RFC 768 UDP RFC 793 TFTP RFC 791 IP RFC 792 ICMP RFC 2068 HTTP RFC 1112 IGMP version 1 RFC 2236 IGMP version 2 RFC 3376 IGMP version 3 RFC 2710 MLD version 1 FRC 3810 MLD version 2 |
| Environment |
| Environment |
| Operating | Temperature: 0 ~ 50 Degree C Relative Humidity: 5 ~ 95% (non-condensing) |
| Storage | Temperature: -10 ~ 70 Degree C Relative Humidity: 5 ~ 95% (non-condensing) |