Specification

Model WNAP-1260 Hardware Specification Interface LAN/WAN: 1 x 10/100Mbps Auto MDI/MDI-X RJ45 port Antenna Gain: 2 x Internal 2dBi Antenna Orientation: Horizontal and Vertical Button / Switch ■ Mode Selection Switch (AP / Repeater / Client) ■ WPS Button ■ Reset button * Push about 3~6 seconds to reset to factory default settings LED Indicators PWR, WPS, Ethernet, WLAN Material Plastic Dimension (W x D x H) 55 x 75 x 40 mm Weight 80g (gross weight) Power Requirement 100~240VAC Power Consumption On-state: 2.1W Low power state: 1.5W Wireless interface Specification Standard Compliant with IEEE 802.11b/g/n Frequency Band 2.4~2.4835GHz Extend Frequency DSSS Modulation Type DBPSK, DQPSK, QPSK, CCK and OFDM (BPSK / QPSK / 16-QAM / 64-QAM) Data Transmission Rates 802.11n(40MHz): 270/243/216/162/108/81/54/27Mbps 135/121.5/108/81/54/40.5/27/13.5Mbps (Dynamic) 802.11n(20MHz): 130/117/104/78/52/39/26/13Mbps 65/58.5/52/39/26/19.5/13/6.5Mbps (Dynamic) 802.11g: 54/48/36/24/18/12/9/6Mbps (Dynamic) 802.11b: 11/5.5/2/1Mbps (Dynamic) Transmission Distance Indoor up to 100m Outdoor up to 300m (Depends on the environment) Channel America / FCC: 2.412~2.462GHz (11 Channels) Europe / ETSI: 2.412~2.472GHz (13 Channels) Japan / TELEC: 2.412~2.484GHz (14 Channels) Channel Width 20 / 40MHz Max. RF Power 802.11b: 17±1.5dBm 802.11g: 14±1.5dBm 802.11n (20MHz): 14±1.5dBm 802.11n (40MHz): 14±1.5dBm Receive Sensitivity 802.11b: -92dBm @ 1Mbps; -85dBm @ 11Mbps, PER < 8% 802.11g: -88dBm @ 6Mbps; -73dBm @ 54Mbps, PER <10% 802.11n: -90dBm @ MCS8; -70dBm @ MCS15, PER <10% Software Features Operation Mode ■ AP/Router ■ Repeater ■ Client (Switchable by Hardware) Wireless Mode ■ Universal Repeater(AP+Client) ■ Repeater(WDS+AP) ■ WDS PTMP(Point to Multipoint) ■ WDS PTP(Point to Point) ■ Client ■ AP(Access Point) Encryption Security ■ WEP (64/128-bit) encryption security ■ WPA / WPA2 (TKIP/AES) ■ WPA-PSK / WPA2-PSK (TKIP/AES) Wireless Security Provides wireless LAN ACL (Access Control List) filtering Wireless MAC address filtering up to 16 entries Supports WPS (Wi-Fi Protected Setup) Enable / Disable SSID Broadcast Wireless Advanced WMM (Wi-Fi Multimedia): 802.11e Wireless QoS Multiple SSID: up to 4 Wireless Isolation: Supports Wireless Isolation IAPP (Inter Access Point Protocol): 802.11f Wireless Roaming Provides Wireless Statistics Max. Clients Wire: 253 Wireless: 32 Internet Connection Type Shares data and Internet access for users, supporting the following internet access: ■ Dynamic IP ■ PPTP ■ Static IP ■ L2TP ■ PPPoE Firewall NAT firewall with SPI (Stateful Packet Inspection) Built-in NAT server supporting Port Forwarding, Port Triggering, and DMZ Built-in firewall with IP address / MAC address / Port / URL filtering Supports ICMP-FLOOD, UDP-FLOOD, TCP-SYN-FLOOD filter, DoS protection Routing Protocol Static Routing VPN Pass-through SIP ALG, PPTP, L2TP, IPSec LAN Built-in DHCP server supporting static IP address distributing Supports UPnP, Dynamic DNS Supports IGMP Proxy System Management Web-Based (HTTP) management interface SNTP time synchronize Easy firmware upgrade Standards Conformance IEEE Standards IEEE 802.11n (2T2R, up to 300Mbps) IEEE 802.11g IEEE 802.11b IEEE 802.11i IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX IEEE 802.3x Flow Control Others Protocols and Standards CSMA / CA, CSMA / CD, TCP / IP, DHCP, ICMP, NAT, PPPoE, SNTP Environment & Certification Temperature Operating: 0 ~ 45 Degree C Storage: -20 ~ 70 Degree C Humidity Operating: 10 ~ 90% (Non-Condensing) Storage: 5 ~ 90% (Non-Condensing) Regulatory CE, RoHS