Specification WNAP-7205

Model WNAP-7205 Hardware Standard support IEEE802.11a/n IEEE 802.3 IEEE 802.3u IEEE 802.3x Chipset Ralink RT2880 Memory 32 Mbytes DDR SDRAM 4 Mbytes Flash PoE Passive PoE Reset Button on PoE Injector Interface Wireless: IEEE 802.11a/n, 1T1R LAN: 1 x 10/100Base-TX, Auto-MDI/MDIX WAN: 1 x 10/100Base-TX, Auto-MDI/MDIX Antenna Internal (Default): 16dBi directional antenna (Vertical Polarization) ■ Horizontal: 60 degree ■ Vertical: 30 degree External (Option): RP-SMA type Connector ■ Switchable by Software ■ For External Antenna Mode, attach antenna before power on. Data Rate 802.11a: 54, 48, 36, 24, 18, 12, 9 and 6Mbps 802.11n (20MHz): up to 72Mbps 802.11n (40MHz): up to 150Mbp Media Access Control CSMA / CA Modulation Transmission / Emission Type: OFDM Data modulation type: OFDM with BPSK, QPSK, 16-QAM, 64-QAM Frequency Band 5.180GHz ~ 5.825GHz Opt. Channel 5.180GHz-CH36 5.200GHz-CH40 5.220GHz-CH44 5.240GHz-CH48 5.260GHz-CH52 5.280GHz-CH56 5.300GHz-CH60 5.320GHz-CH64 5.500GHz-CH100 5.520GHz-CH104 5.540GHz-CH108 5.560GHz-CH112 5.580GHz-CH116 5.600GHz-CH120 5.620GHz-CH124 5.640GHz-CH128 5.660GHz-CH132 5.680GHz-CH136 5.700GHz-CH140 5.745GHz-CH149 5.765GHz-CH153 5.785GHz-CH157 5.805GHz-CH161 5.825GHz-CH165 The 24 channels are defined by the theory. The actual application will vary based on the regulation in different regions and countries. RF Output Power 802.11a: 25 ± 1dBm 802.11n: 22 ± 1dBm Receiver Sensitivity IEEE 802.11a: -90dBm IEEE 802.11n: -88dBm Output Power Control Range 1~100, default:100 Power Requirements 12V DC, 1A (switching) Environment & Certification Operation Temp. Temp.: -20~70 Degree C, Humidity: 10~90% non-condensing Storage Temp. Temp.: -30~80 Degree C, Humidity: 5~90% non-condensing IP Level IP55 Regulatory CE / FCC / RoHS Software LAN Built-in DHCP server supporting static IP address distributing Supports UPnP Supports IGMP Proxy, DNS Proxy Supports 802.1d STP (Spanning Tree) WAN ■ Static IP ■ Dynamic IP ■ PPPoE ■ PPTP ■ L2TP VPN Passthrough ■ PPTP ■ L2TP ■ IPSec Operating Mode ■ Bridge ■ Gateway ■ Ethernet Converter (WISP) Firewall NAT firewall with SPI (Stateful Packet Inspection) Built-in NAT server supporting Port Forwarding (Virtual Server), and DMZ Built-in firewall with Port/ IP address/ MAC/ URL filtering Wireless Mode ■ AP ■ Client ■ WDS PTP ■ WDS PTMP ■ WDS Repeater (AP+WDS) ■ Universal Repeater (AP+Client) Channel Width 20MHz / 40MHz Wireless Isolation Enable to isolate each connected wireless clients Encryption Type 64/128-bits WEP, WPA, WPA-PSK, WPA2, WPA2-PSK, 802.1x Wireless Security Provides wireless LAN ACL (Access Control List) filtering Wireless MAC address filtering Supports WPS (WIFI Protected Setup ) Enable/Disable SSID Broadcast Max. Wireless Client 25 Max. WDS AP 4 Max. Wired Client 60 NTP Network Time Management Management Web UI, DHCP Client, Configuration Backup & Restore, Dynamic DNS Diagnostic tool System Log